## Slide 1
Govt of India
Ministry of Jal Shakti
Department of Water Resources, River Development and Ganga Rejuvenation
CENTRAL GROUND WATER BOARD
Per Drop More Crops
National Workshop
31st May 2023
Sustainable Use of Groundwater
Thakur B. N. Singh
Member (East)

## Slide 2
2

## Slide 3: 437 BCM
60 %
239 BCM
398 BCM
Total annual ground water recharge
Annual extractable ground water resources
Annual Ground Water
extraction
Stage of Extraction
3
*Dynamic Ground Water Resources of India,2022
GROUND WATER OVERVIEW

## Slide 4
Categorization of Groundwater Resource Assessment units | 
Total Assessment units | 7089
Over exploited | 1006 (14 %)
Critical | 260 (04%)
Semi-critical | 885 (12 %)
Safe | 4780 (67 %)
Saline | 158 (02 %)
Chart: 
| Irrigation | Industrial | Domestic
 | 87.169 | 1.5222 | 11.3087
 | 87.169 | 1.5222 | 11.3087
Groundwater Resources of India 2022

## Slide 5: GROUNDWATER USE IN AGRICULTURE
Chart: 
| 1940 | 1950 | 1960 | 1970 | 1980 | 1990 | 2000 | 2010
US | 60 | 70 | 80 | 90 | 100 | 104 | 107 | 107
W.Europe | 45 | 45 | 44 | 43 | 42 | 41 | 40 | 39
Spain | 3 | 4 | 5 | 6 | 8 | 10 | 12 | 14
Mexico | 20 | 23 | 28 | 35 | 42 | 48 | 54 | 58
China | 10 | 12 | 14 | 20 | 35 | 50 | 75 | 90
India | 8 | 12 | 20 | 50 | 100 | 150 | 210 | 260
Pakistan | 3 | 5 | 8 | 15 | 30 | 45 | 60 | 75
Bangladesh | 5 | 9 | 18 | 30 | 45 | 60 | 70 | 80
Sri Lanka | 3 | 3 | 3 | 3 | 4 | 8 | 15 | 25
Vietnam | 2 | 2 | 2 | 4 | 6 | 8 | 15 | 25
Ghana | 1 | 1 | 1 | 1 | 2 | 2 | 6 | 10
South Africa | 5 | 6 | 7 | 8 | 9 | 12 | 17 | 25
Chart: 
| 1991 | 1998 | 2004 | 2009 | 2011 | 2017 | 2020
Stage of Development | 32 | 37 | 58 | 61 | 62 | 63 | 62
Increasing Stage of GW Extraction
India has over 20 million irrigation wells
0.8 million are being added every year.
Every fourth cultivator owns an irrigation well.
Non-owners depend on groundwater markets.

## Slide 6
SUSTAINABLE USE OF GROUNDWATER
The sustainable use of Groundwater refers to the responsible and efficient management of this valuable resource to ensure its long-term availability
Per Capita Water availability in m3/year
Water Stress 1700 m3 year-1
Water Scarcity 1000 m3 year-1
Per Capita Water
Availability in India

## Slide 7: GROUND WATER USE Existing demands and Issues
Deterioration in Ground Water quality
Groundwater table declining in many states
Growing demands for Agriculture,domestic and industrial water supply
Gap in demand and supply of water resources increasing

## Slide 8
High water wastage
  Poor maintenance of pipelines and related leakage issues.
  Lack of water saving awareness.
  Unauthorized tap connections
MISMANGEMENT OF GROUNDWATER

## Slide 9
SUSTAINABLE USE OF GROUNDWATER -OPTIONS
Supply-side Management
Supply-side sustainable use of groundwater works by Increasing the amount of available water.
Demand Side Management
It works on Reducing the amount of water that is being used by stakeholders for its need.
Ground water

## Slide 10
Rainwater Harvesting
Collection and storage of Rainwater
Restricting Run off
Accelerate or induce the process of infiltration by artificial means
Infiltration depends on
Nature of the top soil (infiltration Capacity)
Nature of the Rock (Permeability)
Retention Time
Contact Area
Artificial Recharge
Rainwater Harvesting and
Artificial Recharge to Groundwater
Supply Side Management

## Slide 11
Supply side interventions and water conservation measures through demonstrative projects – CGWB
  Aquifer rejuvenation projects in water stressed districts
  Master Plan for artificial recharge
  Aquifer rejuvenation projects in aspirational districts
  Innovative instream storage - Bridge cum Bandhara
  SOP on source sustainability

## Slide 12
Demand Side Management
  Domestic sector
      Increasing Water use efficiency
      fixing leaky systems or upgrading existing infrastructure to reduce wastage
      Water Pricing /Water cess
      Water meter
      Dual pipe Water supply
  Agriculture sector
      Water use efficiency through drip/sprinkler irrigation
      Conjunctive use
      Less water consuming crops/Crop Rotation
      Setting up Water User association
      Grey water use for irrigation
  Industrial sector
      Adopting water saving technology
      Recycle and reuse of water in industrial process
  Capacity building and Public awareness
  Ground water Regulations
            Regulations, water charge, penalty and EC
Desalination of saline water

## Slide 13
Sustainable Use of Groundwater options
Decrease water demand
Increase water source
Meter water use
Recycle and Reuse
₹
Price water as per use
Water metering
Water efficiency rating
Sensor based efficient showers
Use dish washers
Automatic faucets

## Slide 14
Recycle and Reuse
Greywater is wastewater from non-toilet plumbing systems such as hand basins, washing machines, kitchen, showers and baths.
Can be treated and reused instead of discharging out.
Reusing grey water can decrease groundwater extraction.
SUSTAINABLE USE OF GROUNDWATER -OPTIONS

## Slide 15
ROLE OF CGWB
Monitoring & Assessment
  Strengthening and automation of groundwater monitoring network taken up
    By 2026, CGWB plans to install 9000 automated monitoring stations with the telemetry system
    Under the National Hydrology Project, 5260 DWLRS with telemetry is being installed.
    Annual Groundwater Resources assessment is being carried out

## Slide 16
Through Gazette Notification dated 24th Sept 2020, Central Ground Water Authority (CGWA), for issue of NOC, has introduced the following measures for Regulation in groundwater use by industries/ infrastructure/ mining sectors:
Impact Assessment Report
All industries drawing GW of > 100 m3/day in OCS areas
Annual Water Audit Reports
by industries abstracting GW > 100 m3/day by FICCI, NPC, CII
RWH
As per model building bye-laws.
GW Charges, Penalty, EC
As per specified rates
CGWA and Groundwater Regulation
All industries shall be required to adopt latest water efficient technologies so as to reduce dependence on ground water resources (by at least 20% over the next three years)

## Slide 17
Agriculture Sector: Agriculture sector is exempted from obtaining NOC for GW extraction with views of-
Adopting Participatory approach for sustainable GW management
Review free/ subsidized electricity policy to farmers
Bringing suitable water pricing policy
Working towards crop rotation/ diversification/ other initiatives to reduce over-dependence on groundwater.
CGWA and Groundwater Regulation

## Slide 18
NAQUIM and Aquifer Management Plan
CGWB has carried out National Aquifer Mapping (NAQUIM) in the country and has suggested Aquifer Management Plans (AMP) for the districts.
The NAQUIM outputs and the AMPs have been shared with the district authorities for implementation.
Management Plans are being used for preparation of water security plans under Atal Bhujal Yojana
Under PMKSY-HKKP-GW scheme, the concerned departments in states, especially NER states are using CGWB findings for planning groundwater based irrigation schemes.

## Slide 19
Thank You

## Slide 20
Water Use Efficiency in Agriculture
Direct Seeded Rice (DSR)
System of Rice Intensification in rice(SRI)
Popularizing Micro Irrigation (MI) techniques
Use of MI even in water-intensive crops with more focus on Sugarcane & Banana
Other interventions like Pipe carrying water from source to field to avoid seepage
Selection of low water-intensive crops
Change in cropping pattern